## Slide 1: Echocardiography: An Introduction
Matthew S. haldeman, md MPH

## Slide 2: Echo: overall outline
Part 1
Overview/Anatomy Review
Parasternal Long Axis View
  Technique
  Estimating LV EF
  LA, LVOT, RV size
  LVH screen
Parasternal Short Axis View
  Technique
  3 views
  Method to look for wall motion abnormality, IVS movement, RV size
Apical 4-Chamber View
  Technique
  Valve regurgitation
  RV size, (60% rule, wall thickness), function
Subxiphoid View
  Technique
  Effusion
Part 2
Normal views
Pathology
  LAE
  HFrEF
  HFpEF
  LVH
  Hyperdynamic LV
  LV wall motion abnormality
  RVH
  Elevated R-sided pressure
  MV stenosis
  MV, AV, TV regurgitation
  Effusion
  Tamponade
  PE (McConnell’s sign)
  Thrombus
  Vegetation

## Slide 3: Heart anatomy
Base of Heart
Apex of Heart

## Slide 4: Heart Anatomy

## Slide 5: Echo: some Abbreviations
Chambers
  LV: Left ventricle
  LA: Left atrium
  RV: right ventricle
  RA: right atrium
  LVOT: LV outflow tract
Valves
  MV: mitral valve
  TV: tricuspid valve
  AV: aortic valve
  PV: pulmonary valve
  Others:
    EPSS: E-point septal separation
    TAPSE: tricuspid annular plane systolic excursion
    LVH: left ventricular hypertrophy
    LVMI: left ventricular mass index
    IVS: Interventricular septum

## Slide 6: Echo: basic principles
Image Quality: The 3 questions for every image:
Depth correct?
Gain correct?
Cut correct?
Notes: In echo, image quality is VERY important. If quality is poor, interpretation can be easily misled.
-- Ask yourself these questions on every echo image obtained to ensure quality.

## Slide 7: Echo: simplified method for quick scanning
The 5 E’s:
  Ejection fraction
  Effusion
  Equality (RV vs. LV)
  Exit (aortic root)
  Entrance (IVC)
Notes: I recommend starting here!

## Slide 8: complete 4-view basic Echo: interpretation goals
Chamber size
  LA: dilation?
  LV: dilation? hypertrophy?
  RV: dilation? hypertrophy?
  RV: elevated pressures?
Chamber function
  LV function (systolic: ejection fraction)
  LV function (diastolic)
  LV function (wall motion abnormality)
  RV function
Valves
  MV: stenosis? Regurgitation?
  TV: regurgitation?
  AV: regurgitation?
Effusion
  Present or absent?
  Tamponade present?
IVC
  Elevated R-sided heart pressures or hypervolemia?
  Hypovolemia?
Notes: These are the questions we’re trying to answer with a beside echo. **We will not be doing this with every echo—in an emergent situation, we will only be looking for a few specific things. But This list encompasses the breadth of what we can answer with POCUS

## Slide 9: Positioning, probe, preset
Patient positioning: supine on bed
  Better: Left lateral decubitus position
Ultrasound probe:
  Phased Array probe (or Butterfly probe)
Preset: Cardiac

## Slide 10: Echo: image orientation marker
Notes: Note probe marker is on the opposite side of the image for cardiac imaging

## Slide 11: Echo: 4 major views
Parasternal Long Axis (PLAX)
Parasternal Short Axis (PSAX)
Apical 4 Chamber View (A4CV)
Subxiphoid View (SX)
Notes: There are more views than this in echo. But these are the 4 views of a basic echo.

## Slide 12: Parasternal long axis view (PlaX)

## Slide 13: Parasternal long axis view (PLAX)
Technique:
Place probe to left of the sternum, between ribs 2-5
Direct probe marker towards patient’s R shoulder
Image: University of South Carolina School of Medicine

## Slide 14: Window shopping…
It often requires a lot of probe sliding to find an adequate window to see the heart between the ribs…
Start with large movements to find a window
Once heart is visualized, use fine movements to optimize the image

## Slide 15: Plax view

## Slide 16
LA
LV
LVOT
RV
Inter-
Ventricular
Septum
(IVS)
Mitral Valve
Leaflets
Aortic
Valve (AV)
LV Posterior
Freewall
Descending aorta*
*Indicates depth of image is adequate
Aortic Root

## Slide 17: PLAX view: normal heart
Notes: This is from MH Butterfly 5.19.20

## Slide 18: PLAX view: normal heart
Notes: This is my heart
Good teaching echoes: 8/25/20 (all 4 views are good for CCF); 10/7/20 has really nice PLAX/PSAX views of CCF

## Slide 19: Plax view used for…
Estimating EF (via EPSS)
Evaluating chamber size (LA, LVOT, RV)
Evaluating for LVH (via LVMI)
Screening for valvular disorders
  Look for mitral stenosis
  Can use color doppler to screen for MV/AV regurgitation
    PLAX is the easiest view to see AV regurgitation
    A4CV is best for color doppler to look for MV/TV regurgitation

## Slide 20: Estimating Ejection fraction: e-point septal separation (EPSS)
In PLAX view of normal heart, the MV leaflet tip should almost touch the IVS during diastole
By measuring the shortest distance between MV leaflet tip and IVS, can estimate EF
  EF = 75.5 - 2.5(distance in mm)
  EPSS <5mm, EF = normal (>50%)
  EPSS >7mm, EF <50%
  EPSS >10mm, EF <35%
  EPSS >18mm, EF <30%
  But…confounders:
    AV regurgitation
    MV stenosis
    Thickened IV septum (LVH, Hypertrophic Obstructive CMP)
    MV replacement

## Slide 22: Plax: chamber size
“Rule of Thirds”
  LA, LVOT, and RV should all appear approximately the same size in PLAX view
3
1
2

## Slide 23: Plax: screening for lvh
Left Ventricular Mass Index (LVMI)
  Measure the following parameters at level of MV leaflet tips:
    LV end-diastolic diameter (LVEDD)
    IVS diameter (IVSd)
    LV Posterior Wall diameter (PWd)
  Insert values into calculator, along with pt’s height/weight/gender, to obtain LVMI
  LVMI normal values:
    Male: <115 g/m2
    Female: <95 g/m2
  Calculator:
    http://www.csecho.ca/wp-content/themes/twentyeleven-csecho/cardiomath/?eqnHD=echo&eqnDisp=lvmlvmi
Notes: This calculator will also tell whether it’s eccentric (e.g., dilation) or concentric hypertrophy (e.g., thickened LV walls)

## Slide 24: LVMI measurements
Image: University of South Carolina School of Medicine
LVEDD
IVSd
Pwd
Notes: Measure at level of MV leaflet tips

## Slide 25: Plax: screening for valve regurgitation
Notes: This video loop shows normal flow over the AV—note there is no light blue/orange regurgitant jet re-entering the LVOT from the AV

## Slide 26: Parasternal short axis view (PsaX)

## Slide 27: Parasternal short axis view (psax)
Technique:
From the PLAX probe position, rotate probe 90 degrees so that probe marker is now facing patient’s LEFT shoulder

## Slide 28: Psax: 3 views
PSAX has 3 major views to obtain:
PSAX Aorta (“Mercedes Benz view”)
PSAX Mitral (“Fishmouth view”)
PSAX Mid-Papillary/Apex (“Money view”)
**All are obtained by fanning the probe slightly. The probe itself is stationery on the chest wall

## Slide 29: PSAX: 3 views

## Slide 30: Psax view ANATOMY
PSAX mitral
PSAX aorta
PSAX mid-papillary

## Slide 31: Psax aorta: “mercedes benz view”

## Slide 32: Psax mitral: “fishmouth view”
Notes: This image is my heart during our demonstration from Sept. with Kunka, Mpundu, Zimba

## Slide 33: Psax mid-papillary: “Money view”

## Slide 34: Psax is used for…
Evaluating for wall motion abnormality
  All 4 sides of LV wall should be contracting towards the center of the LV chamber EQUALLY and constrict ~1/3 of width
Evaluating for elevated RV pressure
  Watch IVS: should stay round throughout (should not flatten during diastole)
  Look at LV shape: should stay circular throughout
  Look at RV chamber size in relation to LV size
    Cannot measure RV size here, but can estimate if it appears large…RV diameter should be < LV diameter
Estimating LV EF
  Experts estimate EF from this view by “eyeball method”

## Slide 35: Psax evaluation
RV size
IVS movement
In diastole
Notes: Watch IVS movement in diastole. It should keep a rounded appearance, bulging into the RV lumen in diastole. If it flattens—this is a “D-shaped” septum and indicates elevated R-sided heart pressures

## Slide 36: Psax evaluation
RCA
LAD
LCX
Image: globalultrasoundinstitute.com
Notes: Note coronary vessel distributions when looking for wall motion abnormalities in PSAX

## Slide 37: Estimating EF from psax
https://www.renalfellow.org/2019/08/07/focused-cardiac-ultrasound-abnormalities-on-the-parasternal-short-axis-view/
On this website note:
  Differences in normal vs. depressed LV EF
  Signs of elevated RV pressure

## Slide 38: Apical 4-chamber view (a4cv)
Notes: This is the hardest of all views to obtain (in my opinion!)

## Slide 39: Apical 4-chamber view (a4cv)
Technique:
Place probe at heart apex (5th intercostal space, anterior axillary line, near nipple)
Direct probe marker towards patient’s L axilla, then fan probe towards pt’s R shoulder
Notes: Really nice A4CV: 7/14/2020 in MH Butterfly Archive
--

## Slide 40: A4cv anatomy

## Slide 41: a4cv

## Slide 42: A4cv is used for…
Evaluating RV:
  Size: width of RV should be <60% of LV width at valve level
  Function: Tricuspid Annular Plane Systolic Excursion (TAPSE)
  Hypertrophy: RV freewall thickness
  Other signs of elevated pressures: apical dominance, McConnell sign*
Evaluating valves with color doppler:
  MV stenosis, regurgitation
  AV regurgitation
  TV regurgitation
Evaluating for tamponade*
*will discuss in Part 2

## Slide 43: A4cv: RV size
  Width of RV should be <60% of LV width at valve level

## Slide 44: A4cv: tapse for rv function
Notes: TAPSE: tricuspid annular plane systolic excursion (>17mm is no RV fxn; <16mm is reduced RV fxn)

## Slide 45: A4cv: RV freewall thickness
  Width of RV freewall should be <5mm at end-diastole
  Measure when MV/TV are open

## Slide 46: A4cv: color doppler to look for valve regurgitation
Notes: This is normal color doppler flow over the TV. **No light blue/orange jet regurgitating back into the RA from the RV

## Slide 47: Subxiphoid view (sx) (or subcostal view)

## Slide 48: Subxiphoid view (sx)
Technique:
Place probe in epigastrium, “scoop” under xiphoid process
Direct probe marker towards patient’s L flank

## Slide 49: Sx view anatomy
Notes: The R heart is always adjacent to the liver

## Slide 50: Sx view: normal heart
Notes: Note—sometimes you’ll see a very thin black line between the R heart and the liver, which looks like a small effusion. If it disappears in diastole—is it pericardial fat, not an effusion. If it persists = effusion

## Slide 51: Sx view is used for…
Evaluating for pericardial effusion
  SX view is the BEST to screen for effusion
  Part of eFAST protocol for trauma patient
Evaluating chamber size
  Subjective only
Evaluating valves with color doppler
  Similar to A4CV

## Slide 52: Sx view: where to look for effusion
Will see effusions
In Part 2
Notes: Red arrows: this is where effusion would be
--pericardium is hyperechoic

## Slide 53: basic Echo for beginners
Chamber size
  LA: dilation? (PLAX—Rule of Thirds)
  RV: dilation? (PLAX—Rule of Thirds; A4CV—60% Rule)
  RV: elevated pressures? (PSAX—D-shaped septum and/or RV dilation)
Chamber function
  LV function (systolic: ejection fraction) (PLAX—EPSS)
Valves
  MV: stenosis? Regurgitation? (PLAX--Visualization; A4CV—Color Doppler)
  TV: regurgitation? (A4CV—Color Doppler)
  AV: regurgitation? (PLAX—Color Doppler)
Effusion
  Present or absent? (SX--Visualization)
IVC
  Elevated R-sided heart pressures and/or hypervolemia? (see IVC lecture)
  Hypovolemia? (see IVC lecture)

## Slide 54: Echo for beginners: tasks for each view
PLAX
  Rule of Thirds (for LA, LVOT, RV size)
  EPSS (for LV function)
  MV stenosis
  Color doppler (for MV/AV regurgitation)
PSAX
  Relative RV size vs LV size (for RV dilation from elevated RV pressures)
  D-shaped septum (for elevated RV pressures)
A4CV
  60% rule (for RV size)
  Color doppler (for MV, TV regurgitation)
SX
  Effusion (present or absent)

## Slide 55: Echo for more advanced sonographers
Chamber size
  LA: dilation? (PLAX—Rule of Thirds)
  LV: dilation? hypertrophy? (PLAX--LVMI)
  RV: dilation? (PLAX—Rule of Thirds; A4CV—60% Rule) hypertrophy? (A4CV—RV freewall thickness)
  RV: elevated pressures? (A4CV--apical dominance; PSAX—D-shaped septum and/or RV dilation)
Chamber function
  LV function (systolic: ejection fraction) (PLAX—EPSS)
  LV function (diastolic) (PLAX for LAE and EF, A4CV to assess MV)
  LV function (wall motion abnormality) (PSAX—Visualization)
  RV function (A4CV—TAPSE)
Valves
  MV: stenosis? Regurgitation? (PLAX--Visualization; A4CV—Color Doppler)
  TV: regurgitation? (A4CV—Color Doppler)
  AV: regurgitation? (PLAX—Color Doppler)
Effusion
  Present or absent? (SX--Visualization)
  Tamponade present? (A4CV—Signs of Tamponde)
IVC
  Elevated R-sided heart pressures/cor pulmonale, tamponade physiology? (see IVC lecture)
  Hypovolemia in shock? (see IVC lecture)

## Slide 56: Cardiac pathology…
WILL BE TAUGHT IN PART 2, COMING UP!

## Slide 57: Questions?

## Slide 59: Psax “Mercedes” view anatomy
RV
RA
LA
RVOT
Pulm Trunk